## Slide 1
ASTRA™ is an advanced, non-combustion technology for treating volatile organic compounds (VOCs) and hazardous gaseous pollutants. Using microwave-assisted UV photocatalytic oxidation, it breaks down pollutant molecules at low operating temperatures of below 70°C, without fuel, flames, or water. With treatment efficiency exceeding 95%, ASTRA™ transforms harmful emissions into less harmful byproducts, without generating secondary liquid or solid waste.
Flexible Deployment: Available as fixed plant skids, containerized mobile (OTG) units, compact over-the-top systems, and in-situ solutions for VOC treatment in fume hoods and workbench ventilation systems.
CONTACT US
SELECT YOUR WASTE GAS TO SEE WHAT
CAN DO!
DOWNLOAD BROCHUIRE
Low-Temperature Processing (<70°C): Treats hazardous organic and inorganic gaseous emissions without combustion, open flames, or associated fire hazards.
>95% Treatment Efficiency: Effectively degrades complex VOC mixtures, including ketones, aromatic compounds, and chlorinated species.
Zero Secondary Waste: Eliminates wastewater generation and the need for hazardous spent-carbon disposal.

## Slide 2
Microwave Lysis Technology
Meets industry emission standards and handles complex mixed exhaust gases
Uses microwave & VUV light to break molecular bonds at room temperature
Integrates easily with PLC/DCS systems; plug-and-play with simple maintenance
Flexible design - available as a single unit or modular setup
Achieves up to 99% styrene breakdown with minimal byproduct risk (producing only CO₂ & H₂O)
Low operating cost: electricity plus periodic UV lamp replacement
Working Principle
<70oC
<85%
110-240 V

## Slide 3
Working Principle
<70oC
<85%
110-240 V
Plug-n-Play Pre-treatment Ready Architecture

## Slide 4
SELECT YOUR GAS
OUTPUT
Complete list of Gases treated by

## Slide 5
Gases Treated
Methyl mercaptan | CH4S | 48 | C-S, C-H, H-S | 272,414,339 | H2O, CO2, SO42-
Methyl sulfide | C2H6S | 62 | C-C, C-H, C-S | 332,414,272 | H2O, CO2, SO42-
Phenol | C6H5OH | 94 | ϖ bond, C-H, C-O | 611,414,326 | H2O, CO2
Styrene | C8H8 | 104 | C=C,C-C, C-H, ϖ bond | 611,332,414, | H2O, CO2
Toluene | C7H8 | 92 | ϖ bond, C-H, C-C | 61,14,14,332 | H2O, CO2
Trimethylamine | C3H9N | 59 | C-H, C-N | 414,305 | H2O, N2, CO2
Xylene | C6H4(CH3)2 | 106 | ϖ bond, C-H, C-C | 611,414,332 | H2O, CO2
Gas | Mol. Formula | Mol. Wt. | Main Chemical Bonds | Bond Energies (kJ/mol) | End Products
Ammonia | NH3 | 17 | H-N | 389 | H2O, N2
Aniline | C6H5NH2 | 93 | ϖ bond, C-H, N-H, C-C | <611,414,389,332 | H2O, CO2, N2
Benzene | C6H6 | 78 | ϖ bond, C-H | <611,414 | H2O, CO2
Dimethyl disulfide | C2H6S2 | 94 | S-S, H-S, S-C, C-H | 268,339,268,414 | H2O, CO2, SO42-
Ethyl acetate | C4H8O2 | 88 | C-H, C-O, C=O, C-C | 414,326,728,332 | H2O, CO2
Ethylene oxide | C2H4O | 44 | C=C, C-O, C-H | 611,326,414 | H2O, CO2
Hydrogen Sulfide | H2S | 34 | H-S | 339 | H2O, SO42-
Methanol | CH3OH | 32 | C-H, C-O, H-O | 414,326,464 | H2O, CO2

## Slide 6
Astra vs Conventional Technology
Feature | Thermal Oxidation | VUV Technology
Working Principle | High-temperature thermal oxidation (~760°C+) | Microwave & Ultraviolet (VUV) at room temperature
Pretreatment Needs | Required for particles & oil | Required for particles & oil
System Configuration | Single large unit often preferred for cost-effectiveness | Highly flexible; single unit or multiple modules possible
Footprint | Large (due to ceramic heat recovery beds) | More compact; modular design
Energy Consumption | High fuel demand to maintain temperature; electricity for fans | Primarily electricity (no fuel); lower OPEX
OPEX Drivers | Natural gas, periodic ceramic media replacement | Electricity, periodic lamp replacement
By-product Risks | NOx, potential SO₂ from sulfur content | Minimal; primary by-products are CO₂ and H₂O
Significantly Lower Operating Costs (OPEX)
Compact and Modular Design
Ambient Temperature Operation
Precision Destruction of styrene gas
The Advantage

## Slide 7
Active Installations
Pharmaceutical
Specialty Chemical
Petrochemcial
Products Manufactured
Effluent Gases
Treatment Outcome
Human & veterinary drugs with a primary focus on antibiotic APIs, synthetic drugs formulations
Nitrosylsulfuric acid, Acrylonitrile m-Aminoacetanilide, 1-Aminoanthraquinone , N-Diallyl-2-methoxy-5-acetaminoaniline, etc.
VOCs & odorous compounds
>90% treatment efficiency, reducing exhaust conc. to 0–59 mg/m³.
VOCs, NH₃, H₂S, Phenol
VOCs`
>98% VOC removal, reducing exhaust conc. from 9,837–14,682 mg/m³ to 89.5–246 mg/m³.
Butene, MTBE, Mixed C4 Hydrocarbon, Mixed C5 Hydrocarbons, Mixed Pentenes, Propylene, Ethylene, Methanol, Naphtha
Industries Covered
Pharmaceutical, Specialty Chemical, Petrochemical, Automobile, Power generation, Cement and more.

## Slide 8
INDUSTRY
SOLUTIONS
LABORATORY
SOLUTIONS
MOBILE
SOLUTIONS
One-of-a-kind Industrial Solution
Wide Industry Coverage
Pharma & BioPharma, Electronics – Semicon, Chemical, Power, Cement, Steel etc.
Adapts to diverse VOC and odour treatment applications.
Application-Specific Engineering: Multiple pre-treatment configurations for challenging gas streams
Plug-and-Play Modular Design: Clean, compact, and scalable system architecture
Power-Only Technology: No fuel, water, chemicals, or secondary waste generation.
Sustainable High-Efficiency Operation: Reliable performance, low operating costs and minimal footprint
Compatible with Industrial Automation.
Configurable with PLC &DCS.
I AM INTERESTED

## Slide 9
INDUSTRY
SOLUTIONS
LABORATORY
SOLUTIONS
MOBILE
SOLUTIONS
Fume Hood Companion
No Water Consumption, Wastewater Generation, Carbon Media Replacement or Chemical Dosing
Point-of-source Treatment
Compact & Retrofit Friendly
Low Maintenance Operation
Broad VOC Compatibility
Enhanced EHS Performance
Sustainability-driven Design
Lower Total Cost of Ownership
Destruction of Pollutants.
Not Transfer.
I AM INTERESTED

## Slide 10
INDUSTRY
SOLUTIONS
LABORATORY
SOLUTIONS
MOBILE
SOLUTIONS
The perfect on-the-go unit.
Provides flexibility to move around in the industry unit
No combustion; no flame/flare needed
Works at ambient temperature (ATP)
Suitable for low- medium-high VOC concentrations
Broad VOC Compatibility
Enhanced EHS Performance
Compact system; good for loading racks
No recycling or ETP treatment
Mobile shield against
Hazardous VOC exposure.
I AM INTERESTED